Characteristic Curves- XST Series, 50HZ, 2-Pole

| XST | ～ 2900rpm |
| --- | --- |

Hydraulic Performance Curves

| XST32 – 125 | ～ 2900rpm |
| --- | --- |

Hydraulic Performance Curves

| XST32 – 160 | ～ 2900rpm |
| --- | --- |

Hydraulic Performance Curves

| XST32 – 200 | ～ 2900rpm |
| --- | --- |

Hydraulic Performance Curves

| XST40 – 125 | ～ 2900rpm |
| --- | --- |

Hydraulic Performance Curves

| XST40 – 160 | ～ 2900rpm |
| --- | --- |

Hydraulic Performance Curves

| XST40 – 200 | ～ 2900rpm |
| --- | --- |

Hydraulic Performance Curves

| XST40 – 250 | ～ 2900rpm |
| --- | --- |

Hydraulic Performance Curves

| XST50 – 125 | ～ 2900rpm |
| --- | --- |

Hydraulic Performance Curves

| XST50 – 160 | ～ 2900rpm |
| --- | --- |

Hydraulic Performance Curves

| XST65 – 125 | ～ 2900rpm |
| --- | --- |

- Home

- About Leo

- Events

- News

- Performance

- Exhibition Information

- Products

- Water Pump

- Peripheral Pump

- Centrifugal Pump

- Jet Pump

- SPA Pump

- Domestic Lifting Station

- Pool Pump

- Submersible Pump

- Vertical Multistage Centrifugal Pump

- Stainless Steel Borehole Pump

- Standard Centrifugal Pump

- Stainless Steel Standard Centrifugal Pump

- Stainless Steel Single Stage Centrifugal Pump

- High Pressure Washer

- Triplex Pump

- Accessories

- Garden Machine

- R&D

- Certificates

- Facilities

- Contact Us

- Company Contacts

- Location Map

- Company Dealers

Zhejiang LEO Co., Ltd.

English Français Русский Español Português العربية

窗体顶端

窗体底端

Home » Products » Water Pump » Standard Centrifugal Pump

## Standard Centrifugal Pump

Standard Centrifugal Pump (EN733 – DIN24255)

Bottom

Our standard centrifugal pump is primarily used for circulation and transfer of clean, chemically non-aggressive water and other liquids. It is suitable for water supply and irrigation, water circulation in air conditioning systems as well as for use in auxiliary equipment.

Operating Conditions 
Delivery: up to 220m3/h 
Head: up to 95m 
Liquid temperature 
Standard: -10℃ to 85℃ Upon request: -20℃ to 120℃
Maximum operating pressure: 12 bar(PN12) 
Anti-clockwise rotation when facing pump's suction port
Impeller: AISI304/AISI316
Mechanical seal in compliance with DIN 24960
Lubricated by internal recirculation
Housing sealed by pumped liquid 
Counter flange available on request

Motor 
Three-phase* asynchronous, squirrel cage rotor
Closed construction, external ventilation
Protection class: IP55
Insulation class: 155
Performance in compliance with CEI 2-3(IEC 34.1) 
Max. ambient temperature: +40℃
Overload protection
Compressive type drainage plugs on all motors

Construction Features of Standard Centrifugal Pump 
Single-impeller centrifugal pump is of axial intake and radial discharge 
Inlet and outlet DN conform to EN 733(ex DIN 24255) and UNI 7467
Flanges is in compliance with UNI 2236 and DIN 2532 
Rear entry design (impeller, control valve and motor can be extracted without disconnecting the pump body from the pipes) 

Accessories on Request 
AISI 316 stainless steel or galvanised iron threaded counter flanges
Flanged tapered coupling
Pump and motor sealing gasket

List of Model- XST Series, 50HZ, 2-Pole

| Pump Type | Power | Q = Delivery |
| --- | --- | --- |
|  | kW | HP | Q(l/min) | 0 | 100 | 150 | 200 | 250 | 300 | 400 | 500 | 600 | 700 | 800 | 1000 | 1200 | 1400 | 1600 | 1800 | 2000 | 2300 | 2500 | 3000 | 3600 |
|  |  |  | Q(m3/h) | 0 | 6 | 9 | 12 | 15 | 18 | 24 | 30 | 36 | 42 | 48 | 60 | 72 | 84 | 96 | 108 | 120 | 138 | 150 | 180 | 216 |
| 32-125/07 | 0.75 | 1 | H (m) | 18 | 16.7 | 15.5 | 13.9 | 11.8 | 9.2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 32-125/11 | 1.1 | 1.5 |  | 22.5 | 21.5 | 20.5 | 19 | 17.4 | 15.2 | 9.7 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 32-160/15 | 1.5 | 2 |  | 28.7 | 27 | 25.5 | 23.5 | 21 | 17.8 | 10 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 32-160/22 | 2.2 | 3 |  | 35.7 | 34.3 | 33 | 31 | 28.6 | 25.8 | 19.2 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 32-200/30 | 3 | 4 |  | 46.5 | 43 | 40.5 | 38 | 35.5 | 32 | 24.5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 32-200/40 | 4 | 5.5 |  | 54.5 | 52 | 50 | 47.5 | 45 | 42 | 34.5 | 26 |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 320-250/55 | 5.5 | 7.5 |  | 79 | 74.4 | 71 | 67 | 62 | 55.6 | 37 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 320-250/75 | 7.5 | 10 |  | 99 | 95.3 | 92 | 88 | 83 | 76 | 58.3 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |
| 40-125/11 | 1.1 | 1.5 |  | 14.5 |  |  |  | 13.7 | 13 | 11.3 | 8.8 | 5.8 |  |  |  |  |  |  |  |  |  |  |  |  |
| 40-125/15 | 1.5 | 2 |  | 18.1 |  |  |  | 17.2 | 16.7 | 15 | 12.7 | 9.6 | 6 |  |  |  |  |  |  |  |  |  |  |  |
| 40-125/22 | 2.2 | 3 |  | 24.5 |  |  |  | 23.5 | 23 | 21 | 18.8 | 15.8 | 12.3 | 8.2 |  |  |  |  |  |  |  |  |  |  |
| 40-160/30 | 3 | 4 |  | 31.5 |  |  |  | 30 | 29.5 | 27.5 | 24.5 | 21.5 | 17.4 |  |  |  |  |  |  |  |  |  |  |  |
| 40-160/40 | 4 | 5.5 |  | 38 |  |  |  | 37 | 36 | 34 | 31.5 | 28.5 | 24.5 | 20 |  |  |  |  |  |  |  |  |  |  |
| 40-200/55 | 5.5 | 7.5 |  | 46.5 |  |  |  | 45 | 44 | 41.5 | 38.5 | 34.5 | 29.5 |  |  |  |  |  |  |  |  |  |  |  |
| 40-200/75 | 7.5 | 10 |  | 57 |  |  |  | 55 | 54 | 52 | 49 | 45.5 | 41 | 36 |  |  |  |  |  |  |  |  |  |  |
| 40-250/110 | 11 | 15 |  | 72 |  |  |  | 68 | 67 | 65 | 61 | 67 | 52 | 47 |  |  |  |  |  |  |  |  |  |  |
| 40-250/150 | 15 | 20 |  | 85 |  |  |  | 81 | 80 | 77 | 74 | 70 | 65 | 60 |  |  |  |  |  |  |  |  |  |  |
| 50-125/22 | 2.2 | 3 |  | 17 |  |  |  |  |  |  | 16 | 15.1 | 14 | 12.8 | 9.8 | 6.2 |  |  |  |  |  |  |  |  |
| 50-125/30 | 3 | 4 |  | 20 |  |  |  |  |  |  | 19.5 | 18.8 | 18 | 16.9 | 14.1 | 10.5 |  |  |  |  |  |  |  |  |
| 50-125/40 | 4 | 5.5 |  | 24 |  |  |  |  |  |  | 23.5 | 23 | 22.5 | 21.5 | 19 | 15.8 | 11.8 |  |  |  |  |  |  |  |
| 50-160/55 | 5.5 | 7.5 |  | 32 |  |  |  |  |  |  | 31.5 | 30.5 | 29.5 | 28 | 24.5 | 20.5 | 14.8 |  |  |  |  |  |  |  |
| 50-160/55 | 7.5 | 10 |  | 40 |  |  |  |  |  |  | 39 | 38 | 37 | 36 | 33 | 29 | 24 |  |  |  |  |  |  |  |
| 50-200/110 | 11 | 15 |  | 58 |  |  |  |  |  |  | 55 | 54 | 53 | 50 | 46 | 40 | 33 |  |  |  |  |  |  |  |
| 50-250/150 | 15 | 20 |  | 68 |  |  |  |  |  |  | 65 | 64 | 63 | 61 | 56 | 50 | 41 |  |  |  |  |  |  |  |
| 50-250/185 | 18.5 | 25 |  | 77 |  |  |  |  |  |  | 74 | 73 | 72 | 70 | 66 | 60 | 52 |  |  |  |  |  |  |  |
| 50-250/22 | 22 | 30 |  | 86 |  |  |  |  |  |  | 84 | 83 | 81 | 80 | 75 | 70 | 61 | 51 |  |  |  |  |  |  |
| 65-125/40 | 4 | 5.5 |  | 19 |  |  |  |  |  |  |  |  |  | 17.5 | 16 | 14.5 | 13 | 11 |  |  |  |  |  |  |
| 65-125/55 | 5.5 | 7.5 |  | 23 |  |  |  |  |  |  |  |  |  | 21.5 | 20.5 | 19 | 17.5 | 16 | 14 |  |  |  |  |  |
| 65-125/75 | 7.5 | 10 |  | 27 |  |  |  |  |  |  |  |  |  | 26 | 25 | 24.5 | 23 | 22 | 20 | 18 |  |  |  |  |
| 65-160/110 | 11 | 15 |  | 36 |  |  |  |  |  |  |  |  |  | 35 | 34 | 33 | 31.5 | 30 | 28 | 25.5 |  |  |  |  |
| 65-160/150 | 15 | 20 |  | 42 |  |  |  |  |  |  |  |  |  | 41.5 | 41 | 40 | 38.5 | 37 | 35 | 33 | 29.5 |  |  |  |
| 65-200/150 | 15 | 20 |  | 45 |  |  |  |  |  |  |  |  |  | 46 | 45 | 43 | 41 | 39 | 36.5 | 34 |  |  |  |  |
| 65-200/185 | 18.5 | 25 |  | 52 |  |  |  |  |  |  |  |  |  | 53 | 52 | 51 | 49 | 47 | 44.5 | 42 |  |  |  |  |
| 65-200/220 | 22 | 30 |  | 59 |  |  |  |  |  |  |  |  |  | 60 | 59 | 58 | 56 | 54 | 52 | 49.5 |  |  |  |  |
| 65-250/220 | 22 | 30 |  | 62 |  |  |  |  |  |  |  |  |  | 62 | 60 | 58 | 55.5 | 52 | 48.5 | 44 | 36.5 |  |  |  |
| 65-250/300 | 30 | 40 |  | 76 |  |  |  |  |  |  |  |  |  | 75 | 74 | 73 | 70.5 | 67.5 | 64 | 61 | 54 |  |  |  |
| 65-250/370 | 37 | 50 |  | 90 |  |  |  |  |  |  |  |  |  | 88.5 | 87 | 86 | 84 | 81 | 78 | 74.5 | 68.5 |  |  |  |

Characteristic Curves- XST Series, 50HZ, 2-Pole

| XST | ～ 2900rpm |
| --- | --- |

Hydraulic Performance Curves

| XST32 – 125 | ～ 2900rpm |
| --- | --- |

Hydraulic Performance Curves

| XST32 – 160 | ～ 2900rpm |
| --- | --- |

Hydraulic Performance Curves

| XST32 – 200 | ～ 2900rpm |
| --- | --- |

Hydraulic Performance Curves

| XST40 – 125 | ～ 2900rpm |
| --- | --- |

Hydraulic Performance Curves

| XST40 – 160 | ～ 2900rpm |
| --- | --- |

Hydraulic Performance Curves

| XST40 – 200 | ～ 2900rpm |
| --- | --- |

Hydraulic Performance Curves

| XST40 – 250 | ～ 2900rpm |
| --- | --- |

Hydraulic Performance Curves

| XST50 – 125 | ～ 2900rpm |
| --- | --- |

Hydraulic Performance Curves

| XST50 – 160 | ～ 2900rpm |
| --- | --- |

Hydraulic Performance Curves

| XST65 – 125 | ～ 2900rpm |
| --- | --- |

Installation Dimensions

| Pump Type | Pump | Base | Max. |
| --- | --- | --- | --- |
|  | DNM | DNA | a | h2 | w | x | b | c | c1 | h1 | m | m1 | n | n1 | s | s1 | B | H | L | K |
| XST32-125/07 | 32 | 50 | 80 | 140 | 235 | 129 | 50 | 12 | — | 112 | 100 | 70 | 190 | 140 | 14 | — | 233 | 252 | 443 | 86 |
| XST32-125/11 | 32 | 50 | 80 | 140 | 235 | 129 | 50 | 12 | — | 112 | 100 | 70 | 190 | 140 | 14 | — | 233 | 252 | 443 | 86 |
| XST32-160/15 | 32 | 50 | 80 | 160 | 235 | 129 | 50 | 12 | — | 132 | 100 | 70 | 240 | 190 | 14 | — | 235 | 292 | 443 | 86 |
| XST32-160/22 | 32 | 50 | 80 | 160 | 235 | 129 | 50 | 12 | — | 132 | 100 | 70 | 240 | 190 | 14 | — | 235 | 292 | 443 | 86 |
| XST32-200/30 | 32 | 50 | 80 | 180 | 283 | 121 | 50 | 12 | — | 160 | 100 | 70 | 240 | 190 | 14 | — | 285 | 340 | 461 | 86 |
| XST32-200/40 | 32 | 50 | 80 | 180 | 290 | 133 | 50 | 12 | — | 160 | 100 | 70 | 240 | 190 | 14 | — | 285 | 340 | 187 | 86 |
| XST40-125/11 | 40 | 65 | 80 | 140 | 235 | 129 | 50 | 12 | — | 112 | 100 | 70 | 210 | 160 | 14 | — | 233 | 250 | 443 | 88 |
| XST 0-125/15 | 40 | 65 | 80 | 140 | 235 | 129 | 50 | 12 | — | 112 | 100 | 70 | 210 | 160 | 14 | — | 233 | 252 | 443 | 88 |
| XST40-125/22 | 40 | 65 | 80 | 140 | 235 | 129 | 50 | 12 | — | 112 | 100 | 70 | 210 | 160 | 14 | — | 233 | 252 | 443 | 88 |
| XST40-160/30 | 40 | 65 | 80 | 160 | 283 | 121 | 50 | 12 | — | 132 | 100 | 70 | 240 | 190 | 14 | — | 250 | 292 | 461 | 88 |
| XST40-160/40 | 40 | 65 | 80 | 160 | 290 | 133 | 50 | 12 | — | 132 | 100 | 70 | 240 | 190 | 14 | — | 250 | 292 | 487 | 88 |
| XST40-200/55 | 40 | 65 | 100 | 180 | 311 | 150 | 50 | 12 | — | 160 | 100 | 70 | 265 | 212 | 14 | — | 285 | 240 | 553 | 88 |
| XST40-200/72 | 40 | 65 | 100 | 180 | 311 | 150 | 50 | 12 | — | 160 | 100 | 70 | 265 | 212 | 14 | — | 285 | 240 | 553 | 88 |
| XST40-250/92 | 40 | 65 | 100 | 225 | 278 | 191 | 65 | 14 | — | 180 | 125 | 95 | 320 | 250 | 15 | — | 335 | 405 | 604 | 107 |
| XST40-250/110 | 40 | 65 | 100 | 225 | 278 | 191 | 65 | 20 | — | 180 | 125 | 95 | 320 | 250 | 15 | — | 335 | 405 | 604 | 107 |
| XST40-250/150 | 40 | 65 | 100 | 225 | 208 | 232 | 50 | 22 | 20 | 180 | 260 | 210 | 318 | 254 | 15 | 23 | 335 | 412 | 688 | 107 |
| XST50-125/22 | 50 | 65 | 100 | 160 | 235 | 129 | 50 | 12 | — | 132 | 100 | 70 | 240 | 190 | 14 | — | 255 | 292 | 463 | 92 |
| XST50-125/30 | 50 | 65 | 100 | 160 | 285 | 121 | 50 | 12 | — | 132 | 100 | 70 | 240 | 190 | 14 | — | 255 | 292 | 481 | 92 |
| XST50-125/40 | 50 | 65 | 100 | 160 | 292 | 133 | 50 | 12 | — | 132 | 100 | 70 | 240 | 190 | 14 | — | 255 | 292 | 507 | 92 |
| XST50-160/55 | 50 | 65 | 100 | 180 | 313 | 150 | 50 | 12 | — | 160 | 100 | 70 | 265 | 212 | 14 | — | 285 | 340 | 553 | 92 |
| XST50-160/75 | 50 | 65 | 100 | 180 | 313 | 150 | 50 | 12 | — | 160 | 100 | 70 | 264 | 212 | 14 | — | 285 | 340 | 553 | 92 |
| XST50-200/92 | 50 | 65 | 100 | 200 | 280 | 191 | 50 | 12 | — | 160 | 100 | 70 | 265 | 212 | 15 | — | 305 | 360 | 604 | 92 |
| XST50-200/110 | 50 | 65 | 100 | 200 | 280 | 191 | 50 | 20 | — | 160 | 100 | 70 | 265 | 212 | 15 | — | 305 | 360 | 604 | 92 |
| XST50-250/150 | 50 | 65 | 100 | 225 | 208 | 232 | 50 | 22 | 20 | 180 | 260 | 210 | 318 | 212 | 15 | 23 | 340 | 412 | 688 | 107 |
| XST50-250/185 | 50 | 65 | 100 | 225 | 208 | 232 | 50 | 25 | 20 | 180 | 304 | 254 | 318 | 212 | 13 | 23 | 340 | 412 | 732 | 107 |
| XST50-250/220 | 50 | 65 | 100 | 225 | 208 | 232 | 50 | 28 | 20 | 180 | 304 | 254 | 318 | 212 | 13 | 23 | 340 | 412 | 732 | 107 |
| XST65-125/40 | 65 | 80 | 100 | 180 | 292 | 133 | 65 | 14 | — | 160 | 125 | 95 | 280 | 212 | 14 | — | 285 | 340 | 507 | 105 |
| XST65-125/55 | 65 | 80 | 100 | 180 | 313 | 150 | 65 | 14 | — | 160 | 125 | 95 | 280 | 212 | 14 | — | 285 | 340 | 553 | 105 |
| XST65-125/75 | 65 | 80 | 100 | 180 | 313 | 150 | 65 | 14 | — | 160 | 125 | 95 | 280 | 212 | 14 | — | 285 | 340 | 553 | 105 |
| XST65-160/92 | 65 | 80 | 100 | 200 | 278 | 191 | 65 | 14 | — | 160 | 125 | 95 | 280 | 212 | 15 | — | 331 | 360 | 604 | 112 |
| XST65-160/110 | 65 | 80 | 100 | 200 | 278 | 191 | 65 | 20 | — | 160 | 125 | 95 | 280 | 212 | 15 | — | 331 | 360 | 604 | 112 |
| XST65-160/150 | 65 | 80 | 100 | 200 | 208 | 232 | 50 | 22 | — | 160 | 260 | 210 | 318 | 254 | 15 | 23 | 331 | 392 | 688 | 112 |
| XST65-200/150 | 65 | 80 | 100 | 225 | 208 | 232 | 50 | 22 | 20 | 180 | 260 | 210 | 318 | 254 | 15 | 23 | 335 | 412 | 688 | 112 |
| XST65-200/185 | 65 | 80 | 100 | 225 | 208 | 232 | 50 | 25 | 20 | 180 | 304 | 254 | 318 | 254 | 15 | 23 | 335 | 412 | 732 | 112 |
| XST65-200/220 | 65 | 80 | 100 | 225 | 208 | 232 | 50 | 28 | 20 | 180 | 304 | 254 | 318 | 254 | 15 | 23 | 335 | 412 | 732 | 112 |
| XST65-250/220 | 65 | 80 | 100 | 250 | 208 | 232 | 50 | 28 | 40 | 200 | 304 | 254 | 318 | 254 | 15 | 23 | 332 | 450 | 732 | 112 |

Installation Sketch
Up to 11 kW Included

From 15 kW

Flange Dimensions

PN16 Flanges

| DN | D | M | G | Holes | Max. Thickness |
| --- | --- | --- | --- | --- | --- |
|  |  |  |  | N° | Φ |  |
| 32 | 140 | 100 | 78 | 4 | 18 | 18 |
| 40 | 150 | 110 | 88 | 4 | 18 | 18 |
| 50 | 165 | 125 | 102 | 4 | 18 | 20 |
| 65 | 185 | 145 | 122 | 4 | 18 | 20 |
| 80 | 200 | 160 | 138 | 8 | 18 | 22 |
| 100 | 220 | 180 | 158 | 8 | 18 | 22 |